## Slide 1
Program Interrupts

## Slide 2: Program Interrupt
The concept of program interrupt is used to handle a variety of problems that arise out of normal program sequence.
Program interrupt refers to the transfer of program control from a currently running program to another service program as a result of an external or internal generated request.
Control returns to the original program after the service program is executed.

## Slide 3: Interrupt Procedure
The interrupt is usually initiated by an internal or external signal rather than from the execution of an instruction
the address of the interrupt service program is determined by the hardware rather than from the address field of an instruction;
An interrupt procedure usually stores all the information necessary to define the state of the CPU rather than storing only the program counter.
After a program has been interrupted and the service routine been executed, the CPU must return to exactly the same state that it was when the interrupt occurred.
The state of the CPU at the end of the execute cycle (when the interrupt is recognized) is determined from:
1. The content of the program counter
2. The content of all processor registers
3. The content of certain status conditions

## Slide 4
Program Status Word: The collection of all status bit conditions in the CPU is sometimes called a program status word or PSW. A collection of information that encapsulates the basic execution state of a program at any instant. It permits an interrupted process to resume operation after the interrupt has been handled.

## Slide 5: Types of Interrupt
There are three major types of interrupts that cause a break in the normal execution of a program. They can be classified as:
1. External interrupts
2. Internal interrupts
3. Software interrupts

## Slide 6
External interrupts: External Interrupts come from input-output devices, from a timing device, from a circuit monitoring the power supply, or from any other external source. Examples that cause external interrupts are l/0 device requesting transfer of data, l/0 device finished transfer of data, elapsed time of an event, or power failure. Timeout interrupt may result from a program that is in an endless loop and thus exceeded its time allocation. Power failure interrupt may have as its service routine a program that transfers the complete state of the CPU into a nondestructive memory in the few milliseconds before power ceases.
Internal interrupts: Internal interrupts arise from illegal or erroneous use of an instruction or data. Internal interrupts are also called traps. Examples of interrupts caused by internal error conditions are register overflow, attempt to divide by zero, an invalid operation code, stack overflow, and protection violation. These error conditions usually occur as a result of a premature termination of the instruction execution. The service program that processes the internal interrupt determines the corrective measure to be taken.

## Slide 7: Difference b/w Internal & External Interrupts
Internal interrupt is initiated by some exceptional condition caused by the program itself rather than by an external event.
Internal interrupts are synchronous with the program while external interrupts are asynchronous.
If the program is rerun, the internal interrupts will occur in the same place each time. External interrupts depend on external conditions that are independent of the program being executed at the time.

## Slide 8
Software Interrupt: External and internal interrupts are initiated from signals that occur in the hardware of the CPU.
A software interrupt is initiated by executing an instruction. Software interrupt is a special call instruction that behaves like an interrupt rather than a subroutine call.
It can be used by the programmer to initiate an interrupt procedure at any desired point in the program. The most common use of software interrupt is associated with a supervisor call instruction.
A program written by a user must run in the user mode. When an input or output transfer is required, the supervisor mode is requested by means of a supervisor call instruction.
This instruction causes a software interrupt that stores the old CPU state and brings in a new PSW that belongs to the supervisor mode. The calling program must pass information to the operating system in order to specify the particular task requested.

## Slide 9
Complex Instruction Set Computer (CISC)& Reduced Instruction Set Computer (RISC)

## Slide 10: CISC/RISC
An important aspect of computer architecture is the design of the instruction set for the processor.
Early computers had small and simple instruction sets, forced mainly by the need to minimize the hardware used to implement them. As digital hardware became cheaper with the advent of integrated circuits, computer instructions tended to increase both in number and complexity.
Many computers have instruction sets that include more than 100 and sometimes even more than 200 instructions. These computers also employ a variety of data types and a large number of addressing modes.
The trend into computer hardware complexity was influenced by various factors, such as upgrading existing models to provide more customer applications, adding instructions that facilitate the translation from high-level language into machine language programs, and striving to develop machines that move functions from software implementation into hardware implementation.
A computer with a large number of instructions is classified as a complex instruction set computer, abbreviated as CISC.

## Slide 11
In the early 1980s, a number of computer designers recommended that computers use fewer instructions with simple constructs so they can be executed much faster within the CPU without having to use memory as often. This type of computer is classified as a reduced instruction set computer or RISC.

## Slide 12: Characteristics of CISC
As more instructions and addressing modes are incorporated into a computer, the more hardware logic is needed to implement and support them, and this may cause the computations to slow down. The major characteristics of a CISC processor are:
1. A large number of instructions-typically from 100 to 250 instructions.
2. Some instructions that perform specialized tasks and are used infrequently.
3. A large variety of addressing modes-typically from 5 to 20 different modes
4. Variable-length instruction formats
5. Instructions that manipulate operands in memory

## Slide 13: Characteristics of RISC
The concept of RISC architecture involves an attempt to reduce execution time by simplifying the instruction set of the computer. The major characteristics of a RISC processor are:
1. Relatively few instructions
2. Relatively few addressing modes
3. Memory access limited to load and store instructions
4. All operations done within the registers of the CPU
5. Fixed-length, easily decoded instruction format
6. Single-cycle instruction execution
7. Hardwired rather than microprogrammed control